## Slide 1: Design and Development of low-cost bio inspired soft robot for pipeline inspection
Prepared by : Fadhel Ali, Abdulla Salman
Supervisor: Dr. Belal ElSayed, Dr. Ahmad Abdulrahman

## Slide 2: Introduction
Pipelines are widely used across the oil, gas, water, and sewage industries to transport critical resources over long distances. Regular inspection and maintenance are essential to prevent failures, leaks, and costly downtime. However, many existing inspection methods are invasive, labor-intensive, and pose safety risks especially in narrow or hazardous environments. These challenges highlight the growing need for safer, more adaptable inspection solutions in modern infrastructure systems.

## Slide 3: Literature review
Recent studies highlight the limitations of rigid robots in pipeline inspection, particularly in navigating bends and varying diameters. Xiang (2024) emphasized that most commercial inspection robots use solid metal components, which risk damaging pipes due to friction and lack flexibility.
Yu et al. (2023) demonstrated how soft robots with pneumatic actuators can adapt to confined spaces and irregular paths. Additional research supports the use of hyperelastic materials and bio-inspired designs to improve motion control and safety in pipe environments.

## Slide 4: Problem Statement
Rigid robots used in pipeline inspection are large, inflexible, and unsuitable for small-diameter or curved pipes.
Their metallic bodies risk damaging pipe interiors and often require large access points for insertion.
Manual inspections are hazardous and costly, exposing workers to danger and increasing operational expenses in oil and utility sectors.

## Slide 5: Objectives
Design and simulate radial and linear soft actuators using SolidWorks and ANSYS to evaluate deformation, strain, and stress behavior under pneumatic pressure.
Fabricate actuator components using 3D-printed molds and silicone casting techniques, ensuring fit, flexibility, and seal integrity.
Validate performance through simulation and physical assembly, comparing results to safety thresholds and expected actuator behavior in pipeline environments.

## Slide 6: Radial Shell Balloon Design Overview
Housing for the balloon
Linear Actuator
Gripping pipe walls
Axial motion
Connector
Interface between linear and radial components

## Slide 7: Mold design
Balloon Mold: Two-part cylindrical mold with a centered core to ensure 4 mm wall thickness and a 5 mm air channel. Mold halves were split for safe demolding.
Linear Actuator Mold: Rectangular two-piece mold created using cavity feature. Offset by 2 mm to define wall thickness, with pins and sockets for proper alignment.
Connector Mold: Based on two concentric circles, extruded and separated by a 4 mm lip. Includes a 5 mm internal air channel for integration.

## Slide 8: 3D Printing
We used the printer X1 Carbon to print the parts with the fillet type PLA

## Slide 9: 3D preparation
Some of the printing images show the support according to the print shape.

## Slide 10: Balloon Simulation & Results
Elastic Strain

## Slide 11: Balloon Simulation & Results
Boundary Region | Stress Value (MPa) | Description
Dome/Top Center | 0.0854 MPa | Highest stress zone due to full radial expansion
Mid-Wall Curvature | ~0.04–0.06 MPa | Uniform stress across cylindrical body of the balloon
Base/Fixed Interface | < 0.005 MPa | Minimal stress at the clamped or fixed surface

## Slide 12: Balloon Simulation & Results

## Slide 13: Balloon Simulation & Results

## Slide 14: Linear actuator simulation & Results
Deformation
Boundary Region | Deformation (mm) | Description
Front End (Free Face) | ~242.19 mm | Maximum elongation
Mid-Bellow Sections | ~100–200 mm | Variable expansion across bellows
Back End (Fixed Face) | 0 mm | Fixed support zone, no displacement

## Slide 15: Linear actuator simulation & Results
Elastic strain

## Slide 16: Linear actuator simulation & Results
Stress
Boundary Region | Stress (MPa) | Description
Front End (Top Bellow Face) | 15.818 MPa | Max stress
Mid-Bellows | ~4–6 MPa | Distributed stress along each expanding segment
Back End (Fixed) | < 0.03 MPa | Very low stress at anchor region

## Slide 17: Pouring the mold

## Slide 18: Test the liner part
Initial length:127 mm
Final length:203.2 mm
Extension: 60%

## Slide 19: Assembly
We assembled the pieces via silicon.

## Slide 20: Conclusions
We successfully designed and developed a low-cost, bio-inspired soft robot tailored for pipeline inspection, addressing key challenges in narrow and hazardous environments.
✅ The modular system — including the balloon, linear actuator, and connector — was effectively prototyped using 3D printing and mold casting techniques.
✅ Simulation results showed satisfactory elastic strain, deformation, and stress performance, confirming the design’s feasibility under operational conditions.
✅ The final assembly demonstrated good extension (60% increase in length) and reliable gripping, validating the functional integration of all components.
✅ This work provides a promising foundation for future enhancements, such as automation, sensor integration, and real-world pipeline testing, to further improve adaptability and safety in inspection tasks.

## Slide 21: Recommendations for future research
Integrate Sensors
Incorporate sensors (for leak detection or crack identification) to improve the robot’s inspection capabilities.
Material Improvements
Explore alternative soft materials or composites to increase durability, flexibility, and performance under harsh conditions.
Field Testing
Conduct extensive real-world trials to validate the robot’s reliability, efficiency, and scalability in industrial environments.
Data Analytics Integration
Integrate collected data with AI-driven analytics for real-time assessment, predictive maintenance, and automated reporting.

## Slide 22: Thank you